PTS – No lower than 1500 AGL

Normally performed at 3000 – 3500 MSL

Power on stall- Takeoff configuration

  - Clearing Turn Carb heat on and power back to 1700 rpm

  - Raise nose to maintain altitude

  - Reduce airspeed to about Vx

  - Carb heat off and power to about 2200 RPM (1/2 into the green arc)

  - Add 5-10 degrees bank for turning stalls (PTS says up to 20 degrees)

  - Raise nose to stall horn/buffet

RECOVER

- Lower nose slightly below horizon

- Apply full power and carb heat off

- Accelerate to normal cruise speed

- Straight and level

- Power back to cruise

Power off stall- Landing configuration

  - Clearing Turn

  - Carb heat on and power back to 1700 rpm

  - 10 degrees flaps and stabilize

  - 20 degrees flaps and stabilize

  - 30 degrees flaps

  - Reduce power to idle

  - Add 10 degrees bank if turning stall

  - Raise nose to stall horn/buffet

RECOVER

- Lower nose slightly below horizon

- Apply full power and carb heat off

- 20 degrees flaps and stabilize

- 10 degrees flaps and stabilize

- Flaps up

- Accelerate to normal cruise speed

- Straight and level

- Power back to cruise

Slow Flight/Minimum Controllable Airspeed (MCA)

  - Clearing Turn

  - Carb heat on and power back to 1700 rpm

  - 10 degrees flaps and stabilize

  - 20 degrees flaps and stabilize

  - 30 degrees flaps

  - Wait for stall horn

  - Add power as needed to maintain altitude

  - Change pitch as needed to control airspeed

RECOVER

- Lower nose, full power and carb heat off

- 20 degrees flaps and stabilize

- 10 degrees flaps and stabilize

- Flaps up

- Accelerate to normal cruise speed

- Straight and level

- Power back to cruise

Steep Turns

- Clearing Turn

- Set power to high cruise

- 45 degrees of bank plus or minus 5 degrees

- Add backpressure as you roll through the 30 degree bank mark

- Adjust back pressure and/or adjust bank to maintain altitude.

- Roll out on the same heading you entered (360 degrees of turn)

Forward Slip

- Clearing turn

- Choose a long road with a direct head or tail wind

- Apply rudder till nose is 30-45 degrees right/left of centerline.

- Apply opposite aileron as needed to maintain straight flight/ground path.

Side Slip

- Clearing turn

- Choose a long road with a direct crosswind

- Turn ailerons into wind and use opposite rudder as needed to keep the longitudinal axis parallel with the road (runway).

Notes: Add more or less aileron to slip the airplane sideways while using the rudders to keep the longitudinal axis parallel with the road (runway).

Simulated Engine Out

- Clear area

- Pitch for best glide speed

- Check fuel selector valve and/or switch tanks

- Check mixture control

- Prime in and locked

- Ignition on both

- Radio to 121.5 call Mayday with tail # and location

- Transponder 7700

- Find area to land (land with rows in planted fields).

Unusual Attitude Recovery (Nose High – Airspeed Low)

- Add Power

- Lower Nose

- Level wings

- Then add power and change pitch as necessary to establish cruise flight.

Unusual Attitude Recovery (Nose Low)

- Reduce POWER

- Level wings

- Raise NOSE

- Then add power and change pitch as necessary to establish cruise flight.