GROUND REFERENCE MANEUVERS

600-1000 AGL

S-Turns Along a Road

  - Locate a long road that is perpendicular to the winds at altitude.

  - Clearing turn.

  - Enter maneuver perpendicular to the road at 800’ AGL.

  - As soon as your wings cross the road, begin a coordinated turn to the right or left. You should complete a 180 degree turn or half circle (about 1/4 to 1/2 mile radius), rolling your wings level at the exact point you cross over the road. Your wings will exactly parallel the road. Once your wings have crossed over the road, immediately begin a turn in the opposite direction. You will again complete a half circle, rolling your wings level as you cross the road.

Notes

- When flying downwind, the aircraft should be at its steepest bank in the turn.

- When flying upwind, the aircraft should be at its shallowest bank in the turn.

- The half circles should be symmetrical on each side of the road.

Turns Around a Point

  - Clear the area.

  - Enter the maneuver downwind at 800’ AGL.

  - Pick a visible point away from towns or towers.

  - Maintain a constant radius of the object of 1/4-1/2 mile (about the same distance as on downwind).

  - Circle the point and roll out on your entry heading.

Notes

- When flying downwind, the aircraft should be at its steepest bank in the turn.

- When flying upwind, the aircraft should be at its shallowest bank in the turn.

TAKEOFFS AND LANDINGS

X-Wind Takeoff

- place yoke fully into the wind

- full power

- as speed increases release some of the aileron deflection as needed for x-wind

- ease back on yoke and as a/c flies itself off level wings and crab into the wind

X-Wind Landing

- carburetor heat on (if applicable)

- reduce power opposite spot of intended landing

- set up glide of _______KIAS, 1 notch of flaps

- when 45° key position is reached, turn on to base, second notch of flaps, airspeed ______KIAS

- be aware of wind direction and velocity

- turn to final and add last notch of flaps, airspeed ____KIAS (use min flaps in strong x-wind)

- set up slip with yoke into the wind

- hold directional control with opposite rudder

- maintain ______KIAS until flare

- as airspeed decreases during the flare, you will have to use more yoke pressure into the wind

- after touchdown gradually place the yoke all the way into the wind and hold it there, with full back pressure

Soft Field Take-Off

- apply desired flap setting

- add full backpressure and full power

- keep nose wheel just clear of the ground by releasing some backpressure after nose wheel lifts off

- lift off at lowest possible airspeed

- parallel the ground in ground effect until Vx is attained

- retract flaps, when positive rate of climb (VSI and Altimeter) is achieved or when at least 100 feet AGL and clear of all obstructions and terrain. Once flaps are retracted climb at Vy

Soft Field Landing

- carburetor heat on (if applicable)

- reduce power opposite spot of intended landing

- set up glide of _______KIAS, 1 notch of flaps

- when 45° key position is reached, turn on to base, second notch of flaps, airspeed __KIAS

- turn to final and add last notch of flaps, reduce airspeed to ________KIAS

- touchdown should be made slightly above stall speed so that the nose wheel does not slam into runway surface (you made need to add some power just prior to touchdown to ease the airplane onto the runway)

- the touchdown MUST be with the selected area at minimum rate of descent and minimum airspeed

Short Field Takeoff

- consult performance chart to determine appropriate lift-off and climb speeds and distance required

- se all available runway

- apply flaps as per the POH

- add full power & hold brakes

- lift off and climb at Vx then retract flaps when positive rate of climb (VSI and Altimeter) is achieved or when at least 100 feet AGL and clear of all obstructions and terrain. Once flaps are retracted climb at Vy

Short Field Landing

- carburetor heat on (if applicable)

- reduce power opposite spot of intended landing

- set up glide of _______KIAS, 1 notch of flaps

- when 45° key position is reached, turn on to base, second notch of flaps, airspeed __KIAS

- turn to final and add last notch of flaps, reduce airspeed to ________KIAS

- reduce airspeed to _____KIAS on final with full flaps

- close the throttle during the flare so there is little or no floating before touchdown

- apply brakes, if needed, with control yoke full aft. Keep flaps down if runway is wet or icy, otherwise retract flaps after touchdown

- the touchdown MUST be made beyond and within 200 feet of a specified point

Full Flap Go Around

- carb heat off & apply full power

- flaps 2nd notch and maintain Vx until 100′ agl or obstacle clearance

- gradually retract flaps and accelerate to Vy level off at pattern altitude at cruise airspeed